# Examples
Note: different constraint files for different boards → inside of backend directory
1. Spartan 3A DSP 1800
  1. minsoc/rtl/verilog/minsoc_defines.v
    1. no definitions change, ready to go
  2. minsoc/rtl/verilog/or1200/rtl/verilog/or1200_defines.v (optional, reduce logic use)
    1. uncomment `define OR1200_XILINX_RAMB16
2. Spartan 3E Starter Kit no Ethernet
  1. minsoc/rtl/verilog/minsoc_defines.v
    1. comment `define SPARTAN3A
    2. uncomment `define SPARTAN3E
    3. change CLOCK_DIVISOR from 5 to 2
    4. comment `define ETHERNET
  2. minsoc/rtl/verilog/or1200/rtl/verilog/or1200_defines.v
    1. uncomment `define OR1200_XILINX_RAMB16
    2. uncomment `define OR1200_NO_DC
    3. uncomment `define OR1200_NO_IC
    4. uncomment `define OR1200_NO_DMMU
    5. uncomment `define OR1200_NO_IMMU
3. Spartan 3E Starter Kit with Ethernet
  1. Synthesis properties:
    1. Optimization Goal: Area
    2. Optimization Effort: High
  2. minsoc/rtl/verilog/minsoc_defines.v
    1. comment `define SPARTAN3A
    2. uncomment `define SPARTAN3E
    3. let CLOCK_DIVISOR at 5
    4. change MEMORY_ADR_WIDTH from 13 to 12
    5. uncomment `define ETHERNET
    6. comment `define UART
      1. this is not necessary, though you will get 99% device usage if not commenting, 89% otherwise.
  3. minsoc/rtl/verilog/or1200/rtl/verilog/or1200_defines.v
    1. uncomment `define OR1200_XILINX_RAMB16
    1. uncomment `define OR1200_NO_DC
    2. uncomment `define OR1200_NO_IC
    3. uncomment `define OR1200_NO_DMMU
    4. uncomment `define OR1200_NO_IMMU
    1. comment `define OR1200_MULT_IMPLEMENTED
    2. comment `define OR1200_MAC_IMPLEMENTED
    3. comment `define OR1200_PM_IMPLEMENTED
    4. comment `define OR1200_CFGR_IMPLEMENTED
  2. minsoc/rtl/verilog/ethmac/rtl/verilog/eth_defines.v
    1. uncomment `define ETH_FIFO_XILINX
    2. uncomment `define ETH_XILINX_RAMB4
  3. Collateral effects:
    1. from sw/support/Makefile.inc line 7:
      1. GCC_OPT=-mhard-mul -g to GCC_OPT=-msoft-mul -g
    2. change sw/support/orp.ld:
      1. ram: LENGTH = from 0x00006E00 to 0x00002E00
      2. this is not much memory, I recommend the inclusion of the wb_ddr project to minsoc to use your DDR SRAM memory
    3. change sw/support/board.h
      1. IN_CLK to 10000000	//(10MHz) this will make the simulation have problems with the uart output but will work on implementation
      1. STACK_SIZE to 0x00180
      2. UART_BAUD_RATE to 9600 //baudrate 115200 leads to a high baudrate skew due to a truncation. PC cannot recognize the output
    2. reduce sw/eth.c
      1. remove lines 230-231
      2. remove lines 215-220
      3. remove line 206
      4. remove line 202
      5. change uart_print_long to uart_print_short, line 162
      1. change lines 98 and 99 to char tx_data[64] and char rx_data[64]
      1. remove lines 53-70 void uart_print_long(unsigned int ul) {}
      1. remove lines 31-42 void uart_interrupt(){}
  2. Further area optimization possibilities: (not necessary, DON'T DO)
    1. Turn off: pic, tick timer or debug unit
2. Altera Devices
  1. minsoc/rtl/verilog/minsoc_defines.v
    1. uncoment `define ALTERA_FPGA
    2. comment `define XILINX_FPGA
    3. comment `define SPARTAN3A
    4. select your memory amount "`define MEMORY_ADR_WIDTH 13"
    5. choose a clock division for your global clock related to your design max speed by changing the definition: "`define CLOCK_DIVISOR 5". Since you have an Altera device please use only even numbers for the division, odd numbers are going to be rounded down.
    6. Define your RESET polarity uncommenting "`define POSITIVE_RESET" or "`define NEGATIVE_RESET" and commenting the other.
  2. minsoc/rtl/verilog/or1200/rtl/verilog/or1200_defines.v
    1. uncomment `define OR1200_ALTERA_LPM
    2. include `define OR1200_ALTERA_LPM_XXX