Minimal OpenRISC System on Chip
FAQ

# Adaptation
## How to adapt the firmware to my implementation?
Answer:
1. edit minsoc/sw/support/orp.ld line 14 LENGTH = 0x00006E00 to
  1. your memory amount in Bytes 4 cdot 2^MEMORYADRWIDTH , where MEMORYADRWIDTH is defined in `define MEMORY_ADR_WIDTH in “minsoc/rtl/verilog/minsoc_defines.v”
4 cdot 2^MEMORYADRWIDTH minus ORIGIN = 0x00001200
(e.g. 4*2^13 = 32,768 Bytes = 0x8000 | LENGTH = 0x8000 – 0x1200 = 0x6E00)
1. select your STACK size on “minsoc/sw/support/board.h” line 16 #define STACK_SIZE 0x01000
  1. change your IN_CLK if not using 25000000 (25MHz)

## How to configure the simulation
Answer:
1. configure your system: “minsoc/rtl/verilog/minsoc_defines.v”
  1. You can uncomment ETHERNET on “minsoc_defines.v” to input data to the SoC's Ethernet interface and read data from it.
2. configure “minsoc/bench/verilog/minsoc_bench_defines.v”
  1. Your testbench will use a memory model, not actually the same memory controller the implementation uses. This enables the option “`define INITIALIZE_MEMORY_MODEL”, where the firmware is loaded to the memory before testbench start.
  2. You may use the actual implementation memory:
    1. comment “`define INITIALIZE_MEMORY_MODEL”
    2. edit “minsoc/sim/run/generate_bench”
      1. substitute “../bin/minsoc_model.txt” for “../bin/minsoc_memory.txt”
    3. You might want to uncomment “`define START_UP”, it loads the firmware to a SPI memory. At start of testbench the system reads this memory and loads the firmware to main memory. Takes +-3 min. This is possible to be used for a real system, all you have to do is uncomment “`define START_UP” from “minsoc/rtl/verilog/minsoc_defines.v”.
3. Modify testbench as you please.
  Please refer to “minsoc.pdf” chapter 4 Simulation for more information.

## Is it possible to debug the simulation as I debug the firmware running on my board?
Answer: Yes
Open 3 terminals:
1. terminal 1: from minsoc/sim/run/
  1. ./generate_bench
  2. ./run_bench <your_firmware.hex>
    1. ./run_bench ../../sw/uart/uart-nocache-twobyte-sizefirst.hex
2. terminal 2: from minsoc/sim/run
  1. ./start_server
3. terminal 3: at minsoc/sw/uart
  1. or32-elf-gdb uart-nocache.or32
  2. target remote :9999
  3. load
    1. if you have INITIALIZE_MEMORY_MODEL enabled you don't have to do this
    2. if you have START_UP and waited for the message: “Memory start-up completed...” you also don't need this
  4. set $pc=0x100
  5. c

## My device is full, can I reduce the used logic of the SoC?
Answer: yes
1. configure minsoc/rtl/verilog/or1200/rtl/verilog/or1200_defines.v (recommended values for different devices under synthesis_examples.pdf)
  1. Target FPGA memories (OR1200_XILINX_RAMB16 for Xilinx, Spartan 3 and above, OR1200_ALTERA_LPM for all Altera)
     (if you do this, check: I have generate bench errors, what happened?)
  1. Type of register file RAM (OR1200_RFRAM_GENERIC, OR1200_RFRAM_TWOPORT or OR1200_RFRAM_DUALPORT) (dual port is supported by Xilinx BRAM and Altera)
    (select only one of the three)
    1. if Altera: include `define OR1200_ALTERA_LPM_XXX (right under `define OR1200_ALTERA_LPM if you wish)
  1. comment `define OR1200_PM_IMPLEMENTED
  2. If not using Linux you can:
    1. uncomment `define OR1200_NO_DC
    2. uncomment `define OR1200_NO_IC
    3. uncomment `define OR1200_NO_DMMU
    4. uncomment `define OR1200_NO_IMMU
    5. comment out `define OR1200_CFGR_IMPLEMENTED
  3. If you don't need multiplication, mac operations or divisions
    1. comment out `define OR1200_MULT_IMPLEMENTED
    2. comment out `define OR1200_MAC_IMPLEMENTED
    3. comment out `define OR1200_DIV_IMPLEMENTED
(If you do this, change sw/support/Makefile.inc line 7: GCC_OPT=-mhard-mul -g to GCC_OPT=-msoft-mul -g)

# Problems
## I have generate bench errors, what happened?
Answer:
foo@ubuntu:~/minsoc/sim/run$ ./generate_bench
../../bench/verilog/minsoc_bench.v:590: error: Could not find variable ``minsoc_top_0.or1200_top.or1200_cpu.or1200_rf.rf_a.ramb16_s36_s36.mem'' in ``minsoc_bench.init_fpga_memory''
../../bench/verilog/minsoc_bench.v:591: error: Could not find variable ``minsoc_top_0.or1200_top.or1200_cpu.or1200_rf.rf_b.ramb16_s36_s36.mem'' in ``minsoc_bench.init_fpga_memory''
2 error(s) during elaboration.
foo@ubuntu:~/minsoc/sim/run$

You tried to use the Xilinx RAM or your specific memory, by uncommenting the 'define OR1200_XILINX_RAMB16 or others in the minsoc/rtl/verilog/or1200/rtl/verilog/or1200_defines.v file.
On or1200_r3 the register file, or1200_rf.v, always instantiates a generic memory for DUAL PORT RAM. Previously it instantiated a target specific or generic memory depending on your sets of or1200_defines.v.
Since the CPU does not work if the registers aren't set to zero previous to simulation start, my testbench especifically set the memory content of the registers to zero, before simulation start. I didn't try to find out why this is like that, I only noticed it was that way.
First, I commented out the initialization for dual port RAM to test if the new memory would work. The simulation failed as it did before.
I could include a new initialization for the new memory. Because the new memory is generic and I believe target specific memory should be used whenever possible, I'd recommend you to switch it back to the way it was before and not to touch the memory initializations:
On or1200_rf.v: lines 304 and 280 edit this way:

line 304:
or1200_dpram_32x32
rf_b
(
.rst_a(rst),
.rst_b(rst),
.oe_a(1'b1),
// Port A
.clk_a(clk),
.ce_a(rf_enb),
...

line 280:
/* or1200_dpram #
(
.aw(5),
.dw(32)
)*/
or1200_dpram_32x32
rf_a
(
.rst_a(rst),
.rst_b(rst),
.oe_a(1'b1),
// Port A
.clk_a(clk),
.ce_a(rf_ena),
...
This might be a typo or maybe a work around for something else. That's something the OpenRISC developers have to tell us. It is remarkable that both, OR1200_RFRAM_GENERIC and OR1200_TWOPORT are exactly the way there were before. However, the OR1200_RFRAM_DUALPORT uses now a new module, which is basically an adaptation of the OR1200_RFRAM_GENERIC one, but with DUALPORT, of course.

## MinSoC firmwares won't compile.
Answer: all sw from minsoc has been compiled with the regular GNU toolchain installed by the script under http://www.opencores.org/openrisc,gnu_toolchain . Therefore it uses uClibc not newlib. Precisely that might be your error.

# Tweaks
## I want my design to automatically initialize my firmware on power-up, how do I do that?
Answer: Nowadays there are 3 options to do that:
1. MinSoC comprehends the standard of them which is based on the project OR1k Start-up from OpenCores. At system power-up the CPU's program counter is jumped to the OR1k Start-up module by a Start-up Starter module (inside of minsoc_top.v). The OR1k Start-up contains a hardwired code which reads the data from a SPI memory and copy it to main memory. The amount of data copied is decided upon reading of the first 32 bits of the SPI memory, which must contain the firmware's size. After the code has been completely copied, it restarts the CPU.
  To use this, all you have to do is uncomment “`define START_UP” from “minsoc_defines.v”. Don't forget to load the hex file created by the project's Makefiles into the SPI memory, so actually your firmware is copied to the main memory. The hex file is created from the or32 executable by the project's existing Makefiles.
  Everytime the firmware is updated it has to be uploaded to the SPI memory.
  You can read about it in more detail in the minsoc.pdf file chapter 2.3 Start-Up Modules.
  Advantages: works with any memory type. The speed will be the speed needed by the memory programmer to program the external SPI memory. After that you press the reset button and the firmware will be loaded from the SPI memory by the system. It will then be run.
  Drawback: no debugging, somewhat bigger SoC, required onboard SPI flash.
2. A Xilinx approach has been implemented by Ravi Kumar. A similar Altera approach has been implemented by “sotusotu”. This approach creates a memory initialization file off the firmware executable file, which is then linked to “minsoc_onchip_ram_top.v”.
  Everytime the firmware is changed the synthesizer and P&R must be run for the SoC.
  Link Xilinx: http://opencores.org/forum,OpenRISC,0,3628,0 post 9.
  Link Altera: http://opencores.org/forum,OpenRISC,0,3749 post 5.
  Advantages: once you have a target firmware, it will be on RAM right after FPGA configuration.
  Drawbacks: you have to re-synthesize, re-place&Route to create the bitfile with the firmware, no debugging, only works with onchip-RAM.
3. The XSOC project has yet another approach to pre-initialize the memory with a firmware. They have created a Perl script, that update the SoC resulting bitfile substituting the memory initialization with the target firmware.
  The difference to approach 2 is that approach 2 requires new run of the synthesizer & P&R in order to exchange the firmware, while this directly updates the bitfile result of that very process. After that only a FPGA configuration is necessary to have the new firmware.
  Link: http://pm.stu.cn.ua/wiki/10/Getting_started “Updating bitstream with new software”
  Advantages: high speed,on RAM right after FPGA configuration.
  Drawbacks: no debugging, only works with onchip-RAM.

## I want to compile my firmware independent of MinSoC library but it does not work, what am I doing wrong?
Short example: user “ag1986” says: “test.c
#include stdio.h
int main()
{int a,b,c;
a=5;b=10;
c=a+b;
}
binary generation: “or32-elf-gcc test.c -o test.or32”
simulating using “or1k-sim: or32-elf-sim -f sim.cfg --enable-profile test.or32” does not work.”
Answer: You need a "bootloader" in order to make your software work.

I will try to clearly explain its task in the following lines by comparing it to you running a program on your own operating system.
When you type in the "linux shell" "ls" or "dir" in "windows command prompt", the operating system creates a new process for this program; set a runnable environment for it, with stack, registers and memory; and then at some point set the program counter to the start of your program. (http://en.wikipedia.org/wiki/Process_fork).
The key points here are, you are creating a binary which:
-does not have any information about position in memory
-you are not initializing a stack
-you are not initializing registers
-you are not saying how much memory is available
And without these, your software will simply not work. For instance, if your binary will be located starting at address 0x00, your software will not be ever executed from the beginning by the OpenRISC since it resets to 0x100 and go then onwards until memory finishes.
So, how do I solve this? Generally you cannot directly set registers in C, so you actually need sort of a C assembly mix and then link them together. Furthermore a linker script is used to create memory spaces so you can actually organize the memory dividing data from instruction, exceptions from code and so on.
In the link below you find a small Makefile project with a bootloader and explanation to it in the 5th post.
Link: http://opencores.org/forum,OpenRISC,0,3598
Note: you find more about this in “minsoc.pdf” chapter 3.1 Bootstrapping: a tiny bootloader.
# Advanced Debug System
## I have problems compiling the adv_jtag_bridge, what is going on?
Answer: If you set in Makefile SUPPORT_PARALLEL_CABLES to true, you will need libioperm under Cygwin, for Linux this option is standard.
Under Cygwin: run Cygwin setup.exe and select “libioperm”
If you set in Makefile SUPPORT_USB_CABLES and SUPPORT_FTDI_CABLES to true, you need libusb and libftdi:
Under Linux: install libusb (http://www.libusb.org/) and libftdi
(http://www.intra2net.com/en/developer/libftdi/)
Under Debian based distributions: sudo apt-get install libusb-dev libftdi-dev
Under Cygwin: run Cygwin setup.exe and select “libusb-win32”
-install libftdi from: http://www.intra2net.com/en/developer/libftdi/
## Adv_jtag_bridge does not connect to my cable, why?
Example: 'Failed to find USB-Blaster'
Answer: Nathan Yawn: “It should be possible. The error you are seeing basically means that libUSB enumerated all USB devices, but did not find one with the manufacturer / device ID combo it was looking for (09FB:6001). What are using for your development system?
If it's windows/cygwin, make sure you have a libUSB filter installed for the USBBlaster, then run the libUSB test program and see what devices it shows. If it shows a USBBlaster with a different ID, then you can change the ID in cable_usbblaster.c to match. If it shows nothing, then you need to set up libUSB correctly. If you don't know what it shows, send me the output and I'll take a look.
If you're using Linux, then I think "lsusb" will show all the USB devices in the system. Again, look for a USBBlaster and see if it's ID matches, and if you can't tell what's there, send me the output.”
## Adv_jtag_bridge does not enumerate my device, why?
Example 1: sudo adv_jtag_bridge xpc3
Enumerating JTAG chain...
WARNING: maximum supported devices on JTAG chain (1024) exceeded.
Devices on JTAG chain:
Index Name ID Code IR Length
----------------------------------------------------------------
0: (unknown) 0xFFFFFFFF -1
1: (unknown) 0xFFFFFFFF -1
2: (unknown) 0xFFFFFFFF -1
3: (unknown) 0xFFFFFFFF -1
.
1022: (unknown) 0xFFFFFFFF -1
1023: (unknown) 0xFFFFFFFF -1

Target device 0, JTAG ID = 0xffffffff
ERROR! Unable to autoprobe IR length for device index 0;  Must set IR size on command line. Aborting.

Answer: This implies that you are using the wrong cable or wrong cable support, either you are selecting the wrong cable (xpc3, xess, usbblaster, xpc_usb, ft2232), or you are using the wrong implementation for your cable. That occurs especially on Altera USBBlasters. They have two different implementations, a libftdi based and a libusb based.
You can solve the wrong cable selection by selecting the right cable.
The cable with wrong implementation can be solved by changing adv_jtag_bridge Makefile:
SUPPORT_FTDI_CABLES=true
USE_ALT_FTDI_USBBLASTER_DRIVER=true
Recompile and then try again.
Note: Further information about cables can be found under “rtl/verilog/adv_debug_sys/Software/adv_jtag_bridge/doc/adv_jtag_bridge.pdf”

Example 2: adv_jtag_bridge xpc_usb
Found Xilinx Platform Cable USB (DLC9)
Found Xilinx Platform Cable USB (DLC9)
firmware version = 0x0404 (1028)
cable CPLD version = 0x0012 (18)
Enumerating JTAG chain...
Devices on JTAG chain:
Index   Name            ID Code         IR Length
----------------------------------------------------------------
0:      (unknown)       0x06E5E093      -1
1:      (unknown)       0xF5046093      -1
2:      XC3S500E_FG320  0x41C22093      6
Target device 0, JTAG ID = 0x06e5e093
ERROR! Unable to autoprobe IR length for device index 0;  Must set IR
size on command line. Aborting.

Answer: What occurs here is that the adv_jtag_bridge does not know which protocol the target chip uses. You have two options:
1. That is generally solved by copying the bsdl files into your home directory. In this special case the FPGA chip is the third in the chain, in those cases the bsdl file for the two previous chips are also required for the automatic enumeration. So copying the respective bsdl files for the two remaining chips solves the issue.
2. You input 3 configuration parameters besides of the cable type instead of relying on the bsdl files, for instance “adv_jtag_bridge -x2 -l 2:6 -c 0x02 xpc_usb”. The parameter 'x' informs the device index in the chain, 2 in this example. Then you need to find out (through bsdl file for instance) what is the USER1 command of your chip, xc3s500e_fg320.bsd:612:
“USER1”	(000010),”
The parameter 'l' informs first again the chip index '2' and then the bit width of the chain commands, in this case '6'. Finally, -c informs the USER1 command we just picked out from the bsdl file, it is given in binary format so “2'b10” corresponds to 2 or 0x02 for 6 bit width.

## Adv_jtag_bridge “Ignoring packet error, continuing... “ problem:
Answer: Nathan Yawn: “Ignoring packet error, continuing" means that GDB is timing out waiting for a response from a packet. In adv_jtag_bridge, rsp-server.c, set GDB_BUF_MAX back to it's original value of ((NUM_REGS) * 8 + 1). Smaller packets, done faster, GDB won't have to wait as long. Then, be patient. Things happen very slowly in simulation. Minutes, not seconds.”
Note: same is true for xpc_usb and ftdi usbblaster, it seems.
Static solution:
Nathan Yawn: “In adv_jtag_bridge, open rsp-server.c in a text editor and change the GDB_BUF_MAX back to its earlier value of ((NUM_REGS) * 8 + 1).”
Furthermore, ignore the “Ignoring packet error, continuing...”, it might take time to load depending on the cable.
Dynamic solution:
AhmedHMSoliman: “Use the following command before any other command in gdb to set the remote timeout at the first place.
"set remotetimeout 10"
and you can make sure time out was set to 10 seconds by using the following gdb command:
"show remotetimeout"
after that connect to remote target in the ordinary fashion:
"target remote :9999"”
Furthermore, ignore the “Ignoring packet error, continuing...”, it might take time to load depending on the cable.
## Adv_jtag_bridge self test fails?
Answer: I have the same problem here, do not start adv_jtag_bridge with the “-t” option.
Nathan Yawn: “Yes, there appears to be some incompatibility with the OR1200v3 and the self-test that the Advanced Debug System uses. Since the self-test hasn't changed any, there are two possibilities:
1. The self-test, which was written many years ago for jp2/OR1200v1, depends on some sort of non-spec behavior of the OR1200, which has been 'fixed' in OR1200v3.
2. The OR1200v3 is broken.
I haven't taken the time to figure out which it is, and at this point I'm not sure I care to. I'll try again once the new OR1200 has stabilized.
Warning: even if you disable the self-test, you'll still have problems with ADS and OR1200v3. When I've tried it, the system (repeatably) stops responding the third time I do a stepi. YMMV.”
## Cannot step through instructions after breakpoints, what to do?
Nathan Yawn: “This is a bug in the current versions of the OR1200 CPU (v3). The current version (SVN rev. 388) has a bug related to the hardware single-step function. The maintainers have improved the behavior some, but it's still a problem.
I recommend you checkout an older tag of the OR1200, and use that. Unless there's something in the OR1200v3 you really need, the OR1200v1 will work just fine, and it doesn't have the single-step bug.”